## Slide 1: Town of Marion
Green Communities & the Stretch Energy Code.
March 11, 2025
Lisa Sullivan, Green Communities-
Southeast Regional Coordinator
Mike Rossi, Code Specialist, PSD Consulting
COMMONWEALTH OF MASSACHUSETTS
DEPARTMENT OF ENERGY RESOURCES
Maura Healey, Governor
Kim Driscoll , Lt. Governor
Rebecca Tepper, Secretary
Elizabeth Mahony, Commissioner
Joanne Bissetta, Director

## Slide 3
Green Communities
Designation and Grant Program
3
Grants fund energy efficiency initiatives & renewable energy, innovative projects
Up to $20M/yr in grants to qualifying communities.

## Slide 4
Green Communities
Designation and Grant Program
Designation grant allocations based on a $125k base plus a population/per capita income formula; maximum $1M.
Competitive grants 100K-250k available annually for eligible Green Communities.
Multi year decarbonization grants up to 500k.
New Climate Leader Community Program will offer accelerator grants up to
1 million dollars. Green Communities will need to meet additional criteria to be eligible for these grants. Additional 60 Million in funding reserved for Climate Leader Communities.
Marion has received a 5 grants from Green Communities between 2018 and 2024 totaling $753,556.
($132,672 Designation, $620,884 Competitive

## Slide 5
Climate Act 2021
The legislation signed into law updates the greenhouse gas emissions limits related to the 2008 Global Warming Solutions Act, commits Massachusetts to achieve Net Zero emissions in 2050, and authorizes the Secretary of Energy and Environmental Affairs (EEA) to establish an emissions limit of no less than 50% for 2030, and no less than 75% for 2040.
POLICY BACKGROUND
Notes: The Stretch Energy Code (Stretch Code) regulations have since 2009 been published in MA 780CMR chapters 115.aa and previously 780 CMR 110.aa under the jurisdiction of the Board of Building Regulations and Standards.
The Climate Act of 2021 moved the authority for the Stretch Code promulgation to the Department of Energy Resources (DOER) and at the same time required the development of a new Municipal Opt-in Specialized energy code (Specialized Code). The statute requires that the Specialized Code is formulated to ensure new construction that is consistent with Massachusetts greenhouse gas limits and sub-limits set every five years from 2025 to 2050. The updated Stretch Code is divided into two chapters, following the format of the IECC and appear as new regulations in 225 CMR 22.00 and 225 CMR 23.00.

## Slide 6
2020
Current grid emissions: ~680 lbs./MWh
PROPANE
OIL
GAS
ELECTRIC
RESISTANCE
ELECTRIC
COLD CLIMATE
AIR SOURCE
HEAT PUMP
ELECTRIC
GROUND SOURCE
HEAT PUMP
Pounds of emissions to deliver 1 MMBtu of heat
145
170
120
205
65
45
45% Less
Notes: If we look at the emissions is takes to heat a space using various methods – oil, propane, gas, electric resistance, electric heat pump – electric heat pump today has 45% lower emissions than natural gas.

## Slide 7
2050
Future grid emissions: ~200 lbs./MWh
PROPANE
OIL
GAS
ELECTRIC
RESISTANCE
ELECTRIC
COLD CLIMATE
AIR SOURCE
HEAT PUMP
ELECTRIC
GROUND SOURCE
HEAT PUMP
Pounds of emissions to deliver 1 MMBtu of heat
145
170
120
205
59
65
18
45
13
85% Less
Notes: However, that’s just today – by 2050 with emissions at 200 lbs/MWhr – emissions of heat pumps will be almost 90% less than natural gas.

## Slide 8: Building Energy Code’s role in reducing emissions
Minimize lifecycle costs in new construction
Building code is the primary policy impacting new buildings.
New buildings (built after 2023) ~27% of all building space by 2050
New buildings are easiest and cheapest to make 2050-compliant
New construction market helps drive cost reductions in building retrofits
2030: Massachusetts legal limit is at least 50% reduction in GHG from 1990
Chart: New Construction % of MA total 2024-2050
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
% Existing buildings | 0.98182 | 0.97576 | 0.9697 | 0.96364 | 0.95758 | 0.95153 | 0.94547 | 0.94236 | 0.93926 | 0.93615 | 0.93305 | 0.92995 | 0.92684 | 0.92374 | 0.92064 | 0.91753 | 0.91443 | 0.91286 | 0.91128 | 0.90971 | 0.90814 | 0.90657 | 0.905 | 0.90343 | 0.90186 | 0.90029 | 0.89871
% New Construction | 0.018178 | 0.036356 | 0.054534 | 0.072711 | 0.090889 | 0.10907 | 0.12725 | 0.13656 | 0.14587 | 0.15518 | 0.16449 | 0.1738 | 0.18312 | 0.19243 | 0.20174 | 0.21105 | 0.22036 | 0.22508 | 0.22979 | 0.2345 | 0.23922 | 0.24393 | 0.24865 | 0.25336 | 0.25807 | 0.26279 | 0.2675
Notes: Within the building sector, new construction adds around 1% to the total building space each year. As the chart here shows, that means that around 27% of our expected building space in 2050 has not yet been built.
How we design and construct those buildings with respect to fossil fuels and other greenhouse gas emissions will have a massive impact on achieving our 2050 net zero mandate.
Since we literally design these buildings from the ground-up, they are far easier and cheaper to build to have net zero emissions than the work and cost of renovating our existing (and in many cases historic) buildings.
In addition to being the buildings that we can most easily build and operate without fossil fuels, the techniques, materials and equipment used to build new buildings to net-zero provides the scale to drive down the costs of retrofit work in existing buildings. For example, as we grow the supply chain for heat pumps for new buildings, that also reduces the cost and increases the number of skilled contractors to install heat pumps in existing building renovations.

## Slide 9
Massachusetts Building Energy Code Adoption by Municipality

## Slide 10
Base, Stretch, and Specialized – 3 Options
  New construction only
  48 municipalities so far
Specialized Code
(Stretch code + additions)
  New construction, major renovations/additions for GC municipalities and adopters
  253 municipalities
Stretch Code (IECC 2021+ MA amendments)
  New construction for non-GC municipalities
  50 municipalities
Base Code (IECC 2021 + MA amendments)
Marion

## Slide 11
3 tiers of Energy Code
available to MA towns & cities:
Massachusetts "Opt-In" Energy Codes
Stretch Code
IECC 2021
w/ key MA amendments:
225 CMR Chapter 22 (residential)
225 CMR Chapter 23 (commercial)
61% population
New Construction,
Major Alterations & Additions
253 municipalities
30% population
New Construction Only
48 municipalities
9% population
50 municipalities
Specialized Code
IECC 2021
w/ key MA amendments:
225 CMR Chapter 22 +
Appendix RC (residential)
225 CMR Chapter 23 +
Appendix CC (commercial)
IECC 2021 (10th edition*)
w/ MA amendments:
Base Code
Reference Stretch Code for
existing buildings
Notes: For simplicity we are referencing the 10th edition of the Base Code. The 9th edition is still available for projects permitted up until June 30, 2025 and uses the older IECC2018 as it's energy code with MA amendments. After July 1, 2025 the 10th edition will be the only base energy code in effect.

## Slide 12
  Summer 2024: Posted draft guidelines for public comment
  Fall 2024: Submitted Draft regulations to Joint TUE committee and posted on the DOER website for public review
  Fri 14 Feb 2025: Secretary of State promulgated updated regulations
TIMELINE:
Updates effective February 14, 2025

## Slide 13: What is a HERS Rating? (Home Energy Rating System)
Annualized energy analysis
Heating, cooling, water heating
Lighting and appliances
Reference Home
Based on IECC 2006 Code
(International Energy Conservation Code) Defined as 100 Points
1 percent change in consumption = 1 point
HERS 51 means about
49% more efficient than reference home
2021 Ave. MA home = 51
(2006)

## Slide 14: Why Test Performance?
Prescriptive codes don’t guarantee good installation,
air and water tightness,
or that thermal insulation is effective.
Small air gaps can
reduce insulation R-values by 50% or more.
HERS Raters provide third party verification

## Slide 15
Residential Low-Rise Stretch Code
Compliance Pathways:
New Construction Permits – IECC/Stretch Code Chapter 4: | 
New Dwelling units | HERS rating
Group R1 transient use e.g. hotel/motel | Prescriptive (REScheck)
Any building | Passive House (Phius or PHI)
Existing Building Permits – IECC/Stretch Code Chapter 5: | 
Major additions, Major alterations, Change-of-use | HERS rating
Small additions, Small alterations, Historic buildings, Group R1: alterations, additions | Prescriptive (REScheck)
Any building | Passive House (EnerPHit, PHI or Phius)

## Slide 16
Updates to Residential
HERS Rating Requirements

## Slide 17
Updates to Residential
Prescriptive changes
This exception for Alterations also applies to Major Alterations, Additions, or Change of Use that would otherwise trigger a HERS rating on Table R406.5 but are determined to be Historic Buildings by a governing authority.

## Slide 18
Updates to Residential
Clarifying When a HERS Rating is/isn’t Required
An existing house with an unconditioned basement will be remodeled. The basement is 1,200 SF and will be insulated and fully conditioned. This does NOT trigger a HERS rating because the existing basement is not growing in SF.
If an addition is added to the house with a full basement connecting to the existing basement, and the new larger basement is conditioned, the project will require a HERS rating.

## Slide 19
Updates to Residential
Clarifying When a HERS Rating is/isn’t Required
If a dormer is added to the existing roof, thereby increasing the occupiable SF of the existing attic, and the attic is insulated and finished to become part of the conditioned building envelope, this WILL trigger a HERS rating.
An existing attic space, 1200 SF, will be finished and insulated so that it is part of the conditioned building envelope. No changes to the roof will be made to "grow" the space. This does NOT trigger a HERS rating.

## Slide 20
HERS rating updates:
1. HERS credit for embodied carbon in new construction: 3 HERS points for either insulation or concrete
2. ADU HERS maximum for Accessory Dwelling Units: HERS 52-58
3. HERS ratings for existing building permits in Chapter 5 are relaxed: HERS 65-75
4. Exception for historic homes allows them to follow the prescriptive path
Prescriptive path updates:
5. Ceiling R-value reduced from R-60 to R-49
6. SHGC for windows – no maximum required
The following are some of the more notable changes from the 2023 Stretch Code found in the 2025 Stretch Code update:
Significant Updates:
Residential Low-Rise

## Slide 21
Updates to Residential
Clarifying When a HERS Rating is/isn’t Required
This means if a project satisfies both a + b, then it triggers HERS:
a
work area is
>50% of
existing project
b
+
Exceeds 1,000 SF
or
Exceeds 100% of the existing conditioned floor area
=HERS

## Slide 22
Updates to Residential
Accessory Dwelling Unit HERS Rating:
Stand-alone ADU
ADU attached to existing house
HERS
52/55/58
HERS
52/55/58
Existing house is separate from the attached ADU and is NOT included in the HERS rating.
Existing
House

## Slide 23
Updates to Residential
Bonus 3 HERS points for Embodied Carbon: net zero insulation
Buildings typically use one or two insulation types for above grade walls and ceilings, and different board insulation products below-grade. In order to achieve insulation that is net zero embodied carbon, typically the carbon storage above grade must exceed the carbon content embodied in the below grade insulation.
DOER will provide a standard calculation sheet, to enter values from Table R406.5.3 or from product EPDs to show the insulation products used by area (Square meters) and then calculate whether the net GWP is positive or negative. Homes where total insulation is net negative earn the 3 bonus HERS points.

## Slide 24
Updates to Residential
Bonus 3 HERS points for Embodied Carbon: Concrete
Example EPD
Many of the concrete ready-mix suppliers in Massachusetts have invested in providing Environmental Product Declarations (EPDs) for their concrete ready-mix products. If a project selects ready-mixes that are lower in embodied carbon than the Eastern Region average, shown in Table R406.5.4 then they qualify for 3 bonus HERS points.
Copies of the relevant concrete EPDs must be shared with the HERS rater and building inspector.
Notes: EMbodied Carbon for concrete – baseline is shown in TABLE R406.5.4 DEFAULT CONCRETE GLOBAL WARMING POTENTIAL VALUES
aThese numbers are 100% of the Eastern Region average GWP figures from the National Ready Mix Concrete Associations' "A Cradle-to-Gate Life Cycle Assessment of Ready-Mixed Concrete Manufactured by NRMCA Members, Version 3.2," (July 2022), pg. 65. NRMCA_LCAReportV3-2_20220224.pdf

## Slide 25
Applications: Small Additions / Alterations / Historic Buildings
Updates to Residential
Prescriptive Insulation R (& U) Values

## Slide 26
R403.6 Ventilation requirements: Now reference AHRI standard 1060.
R404.4 EV ready spaces: Now allows NACS(Tesla) or J1772 EV charger, or NEMA electric outlet.
R405.2 Passive House certification: Revised language/corrected wording for PHI and Phius certifications.
R405.3 Near Passive House documentation: Compliance path for projects narrowly failing Passive House certification.
Stretch code: Residential Low-Rise
R501.2 & R506 Adds EnerPHit compliance option for existing building permits.
R503.1.1 Exception allows min. of R-3.7/inch insulation in exposed cavities.
Stretch code: Existing Building Alterations
Summary of Other Updates:

## Slide 27
Upcoming Trainings:
www.masssave.com/en/trade-partners/events-and-trainings-calendar?page=1
On-line training tomorrow!
Go here to find more info on more trainings:
email anytime for help:
stretchcode@mass.gov
or
psdtraininghelpma@psdconsulting.com

## Slide 28
Timeline for updated Technical Guidance documents is late March 2025 through June 2025
New Technical guidance materials:
    Calculation of embodied carbon credits (R406 HERS & C406 options)
    Templates for District Energy Systems – DOER order of conditions application
    Revised/expanded case studies for residential additions/alterations
UPDATES TO TECHNICAL GUIDANCE

## Slide 29
Appendix A
Commercial Stretch Code

## Slide 30
Commercial STRETCH CODE updates to Mechanical and Electrical (C403 & C405):
C403.3.2 Approved Software Calculation Tables (8) and (9); Updates the reference tables for VRF air conditioners (table 8) and heat pumps (table 9) from IECC 2021 to IECC 2024 versions to reflect recent changes in the testing standards used.
C403.7.4. Energy Recovery Systems. Enthalpy Recovery Ratio and Sensible Energy Recovery Ratios are better defined in these sections per feedback from various HVAC public comments. The required values and ventilation rates are fine-tuned per this feedback as well.
C405.13 EV Ready Spaces. Adds Tesla (NACS) standard as a charging option.
Commercial Stretch Code
Mechanical Updates

## Slide 31
Commercial STRETCH CODE updates to credit options (C406):
C406.1 Additional energy efficiency credit requirements. Embodied carbon credits are added as additional options to the commercial code in response to several requests received in public comments.
C406.13 Low GWP concrete mix. This section is added to provide an embodied carbon credit incentive in accordance with C406.1.
C406.14 Net zero GWP insulation. This section is added to provide an embodied carbon credit incentive is accordance with C406.1.
C406.2.3. Renewable space heating. This section is amended to state that electric resistance shall not be used except for defrost function, and to note that the COP value at 5F shall be the COP of the outdoor unit of the cold-climate air source heat pump.
Commercial Stretch Code
C406 Credit Options

## Slide 32
Commercial STRETCH CODE updates to District Energy Systems (C407.2):
C407.2.1 Electrification and documentation for highly ventilated buildings. An exception is added that allows District Energy Systems (DES) that include an inter-building heat recovery function (a DES that is able to use excess heat from one building for useful heating in other buildings) to be exempted from the partial electrification requirement for highly ventilated buildings. Examples of DES’s that are planning to include inter-building heat recovery include: Harvard University, Tufts University, and some state-owned systems, and typically requires conversion of building HVAC systems to be compatible. This has received strong support from various DES stakeholders.
Commercial Stretch Code
District Energy Systems

## Slide 33
Commercial STRETCH CODE updates to Passive House + HERS performance paths (C407.3 & C407.4):
C407.3 Passive House. DOER received a lot of feedback on the specific wording for both Phius and PHI compliance, in addition to a large amount of support for a “third option” for compliance. This “third option” will allow projects to proceed through funding and final occupancy, where projects narrowly fail to meet the full Passive House certification standards but still exceed other building code performance pathways.
C407.4 HERS Index for multi-family buildings. The HERS ratings are relaxed to incentivize the use of embodied carbon credits, and ease the requirements on for major alterations, additions or change-of use projects. This has received broad and very positive feedback. A note has been added to Table C407.4 allowing historic buildings to follow the prescriptive compliance pathway. Finally, references to residential chapters in the footnotes are updated to reference commercial chapters at the request of designers.
Commercial Stretch Code
Passive House & HERS

## Slide 34
Commercial Stretch Code
HERS Rating Requirements

## Slide 35
Commercial STRETCH CODE updates to existing building alterations, additions and change-of-use permits (IECC Chapter 5):
C502.3.7 Air Infiltration Testing. Clarifies that air infiltration testing on additions is for the addition only.
C503.1 General. Clarifies how and when Alterations trigger the requirements of Chapter 4. Most of the text is from IECC 2021, but item 7 is added to allow limited openings into walls without having to then upgrade the entire structure.
C503.2.4 Derating and Thermal Bridges. This new provision allows thermal bridges that are inaccessible to not have to count toward derating calculations.
C505.1 General. This Change-of-use text from IECC 2021 is amended to add the term “total modeled annual” before both “fossil fuel use” and “energy use”. The unamended text was vague and created some confusion. This update allows many tenant fit outs to occur without triggering the entire building envelope to be upgraded. Further, an exception is added that allows new windows (and upgrading the thermal quality of the connection of the window to surrounding wall) without triggering a whole envelope upgrade.
C506 EnerPHit Standard. Added in response to stakeholders requesting that the EnerPHit Standard (a PHI version of Passive House for existing buildings) be sanctioned within the code.
Commercial Stretch Code
Existing Buildings (Chapter 5)

## Slide 36
Appendix B
Residential Cost Analysis -Comparing the Base Code to Stretch Energy Code

## Slide 37: Large Single Family - Electric
MA 10th Edition Building Code | 2025
Home Details
4000 ft2
Large Single Family
5 Bedrooms
Worcester, MA
 | COSTS |  | BENEFITS5 | NET
Total Added Construction Costs or Savings | $3,062 Cost Savings |  | $12,000 Rebates1,4 | $15,062 Savings Compared to Base Code
HOME BUYER | $1,506 Reduction to Downpayment3 | $1,012 Reduction to Annual Mortgage Payment3 | $379 Estimated Additional Energy Costs per Year2 | $633 Buyer Annual Net
Costs and Benefits to Meet Stretch Code*
1. Rebates are calculated on a per unit basis, using Mass Save ® new construction program Base Tier Incentives of $7,500 without any Market Transformation Adders. These incentives are not applicable to mixed fuel projects.
Energy costs are based on 28.7 cents/kWh, $2.08/therm, and $3.62/gal propane
30-year mortgage assumes 10% down payment at 6.35% APR
In addition to the Mass Save ® rebates, projects may be eligible for $2,500/unit rebate as part of the 45L Federal Tax Credit.
Additionally, projects with ASHPs may be eligible for a Federal 30% Tax Credit of the ASHP install, up to $2,000.
Mass Save Incentives are not available in communities with municipal light plans, which are locally owned utilities which represent 52 towns that make up about 13% of the MA population.
HERS Index (ERI)
52 42
Base Stretch
Electric
Heat Pump
*Green shaded boxes indicate cost savings, while red shaded boxes indicate added costs.

## Slide 38: Large Single Family - Electric
MA 10th Edition Building Code | 2025
4000 ft2 Large Single Family
5 Bedroom - Worcester, MA
FEATURE | BASE CODE3 | STRETCH CODE4 | COST DIFFERENTIAL1
HERS INDEX | 52 | 42 | 
Windows (U-Value/SHGC) | U-0.25, 0.29 SHGC | U-0.28, 0.29 SHGC | -$4,110
DHW | Gas Tankless 0.94 EF | HPWH, 50 gal, 2.35 EF | -$316
Heating | Gas, 98% AFUE | SEER 20, 12 HSPF, Ducted | -$35
Cooling | SEER 14.2 |  | 
Duct Leakage to Outside | 2 CFM25 per 100ft2, R-6 | In Conditioned Space* | $0
Foundation Insulation | NA | NA | $0
Floor Insulation | R-30 Fiberglass Batt | R-30 Fiberglass Batt | $0
Walls Insulation | R-21, 2x6, 16 in o.c. | R-21, 2x6, 16 in o.c. | $0
High Efficacy Lighting | 100% LED | 100% LED | $0
Ceiling Insulation | Ceiling R-49, Vented | R-38 Open Cell Spray Foam, Unvented | -$1,847
Air Infiltration | 3 ACH50 | 1.5 ACH50 | $3,246
Mechanical Ventilation | HRV, 75% | HRV, 75% | $0
Pre-Wiring5 | N/A | N/A | $0
Solar Array5 | N/A | N/A | $0
TOTAL |  |  | -$3,062
Electric
Heat Pump
Breakdown of Construction Costs to Meet Stretch Code
Additional Cost are the costs above Base Code to reach Stretch Code.
Cost included in basement and/or attic thermal boundary change
Base Code home features are based on an analysis of typical practices for achieving a HERS 52 using HERS Provider data on pre viously built
homes in Massachusetts.
Stretch Code home features are based on cost optimization modeling using BEopt software. Some individual features are less efficient than the Base Code home, but they are more than offset by other features that are more efficient. One benefit of using a HERS Index ta rget as the basis of the Stretch Code is that it give builders the flexibility to make different design choice to allow for optimization of cost e ffectiveness, work around other design constraints, and accommodate client-specific requests. The stretch code model was developed used REM/rate Version 16.1.1.
Pre-wiring and solar costs are only applicable to mixed fuel projects following the Specialized code and do not apply to the Base or Stretch Code.
HERS Index (ERI)
52 42
Base Stretch

## Slide 39: Large Single Family - Gas
MA 10th Edition Building Code | 2025
 | COSTS |  | BENEFITS5 | NET
Total Added Construction Costs | $10,892 Extra Costs |  | $2,500 Rebates1,4 | $8,392 Cost Compared to Base Code
HOME BUYER | $839 Increase in Downpayment3 | $563 Increase in Annual Mortgage Payment3 | $598 Estimated Energy Cost Savings per Year2 | $35 Buyer Annual Net
1. Rebates are calculated on a per unit basis, using Mass Save ® new construction program Base Tier Incentives of $7,500 without any
Market Transformation Adders. These incentives are not applicable to mixed fuel projects.
Energy costs are based on 28.7 cents/kWh, $2.08/therm, and $3.62/gal propane
30-year mortgage assumes 10% down payment at 6.35% APR
In addition to the Mass Save ® rebates, projects may be eligible for $2,500/unit rebate as part of the 45L Federal Tax Credit.
Mass Save Incentives are not available in communities with municipal light plants, which are locally owned utilities which represent 52 towns that make up about 13% of the MA population
Gas
Costs and Benefits to Meet Stretch Code*
Home Details
4000 ft2
Large Single Family
5 Bedrooms
Worcester, MA
HERS Index (ERI)
52 42
Base Stretch
*Green shaded boxes indicate cost savings, while red shaded boxes indicate added costs.

## Slide 40: Large Single Family - Gas
MA 10th Edition Building Code | 2025
FEATURE | BASE CODE3 | STRETCH CODE4 | COST DIFFERENTIAL1
HERS INDEX | 52 | 42 | $0
Windows (U-Value/SHGC) | U-0.25, 0.29 SHGC | U-0.18, 0.29 SHGC | $4,951
DHW | Gas Tankless 0.94 EF | Gas Tankless 0.94 EF | $0
Heating | Gas, 98% AFUE | Gas, 98% AFUE | $0
Cooling | SEER 14.2 | SEER 16 | $553
Duct Leakage to Outside | 2 CFM25 per 100ft2, R-6 | In Conditioned Space* | -$361
Foundation Insulation | NA | NA | $0
Floor Insulation | R-30 Fiberglass Batt | R-30 Fiberglass Batt | $0
Walls Insulation | R-21, 2x6, 16 in o.c. | R-21, 2x6, 16 in o.c., R-5 XPS | $4,728
High Efficacy Lighting | 100% LED | 100% LED | $0
Ceiling Insulation | Ceiling R-49, Vented | R-38 Open Cell Spray Foam, Unvented | -$2,226
Air Infiltration | 3 ACH50 | 1.5 ACH50 | $3,246
Mechanical Ventilation | HRV, 75% | HRV, 75% | $0
Pre-Wiring5 | N/A | N/A | $0
Solar Array5 | N/A | N/A | $0
TOTAL |  |  | $10,892
Gas
Additional Costs are the costs above Base Code to reach Stretch Code. .
Cost included in basement and/or attic thermal boundary change
Base Code home features are based on an analysis of typical practices for achieving a HERS 52 using HERS Provider data on pre viously built homes
in Massachusetts.
Stretch Code home features are based on cost optimization modeling using BEopt software. Some individual features are less efficient than the Base Code home, but they are more than offset by other features that are more efficient. One benefit of using a HERS Index target as the basis of the Stretch Code is that it give builders the flexibility to make different design choice to allow for optimization of cost effec tiveness, work around other design constraints, and accommodate client-specific requests. The stretch code model was developed used REM/rate Version 16.1.1.
Pre-wiring and solar costs are only applicable to mixed fuel projects following the Specialized code and do not apply to the Base or Stretch Code.
Breakdown of Construction Costs to Meet Stretch Code
4000 ft2 Large Single Family
5 Bedroom - Worcester, MA
HERS Index (ERI)
52 42
Base Stretch

## Slide 41: Small Single Family - Electric
MA 10th Edition Building Code | 2025
 | COSTS |  | BENEFITS5 | NET
Total Added Construction Costs | $11,597 Cost Savings |  | $12,000 Rebates1,4 | $23,597 Cost Compared to Base Code
HOME BUYER | $2,360 Reduction to Downpayment3 | $1,586 Reduction to Annual Mortgage Payment3 | $242 Estimated Additional Energy Costs per Year2 | $1,344 Buyer Annual Net
1. Rebates are calculated on a per unit basis, using Mass Save ® new construction program Base Tier Incentives of $7,500 without any
Market Transformation Adders. These incentives are not applicable to mixed fuel projects.
2. Energy costs are based on 28.7 cents/kWh, $2.08/therm, and $3.62/gal propane
30-year mortgage assumes 10% down payment at 6.35% APR
In addition to the Mass Save ® rebates, projects may be eligible for $2,500/unit rebate as part of the 45L Federal Tax Credit. Additionally, projects with ASHPs may be eligible for a Federal 30% Tax Credit of the ASHP install, up to $2,000.
Mass Save Incentives are not available in communities with municipal light plans, which are locally owned utilities which represent 52
towns that make up about 13% of the MA population
Home Details
2100 ft2
Small Single Family
3 Bedrooms
Worcester, MA
Costs and Benefits to Meet Stretch Code*
Electric
Heat Pump
HERS Index (ERI)
52 42
Base Stretch
*Green shaded boxes indicate cost savings, while red shaded boxes indicate added costs.

## Slide 42: Small Single Family - Electric
MA 10th Edition Building Code | 2025
FEATURE | BASE CODE3 | STRETCH CODE4 | COST DIFFERENTIAL1
HERS INDEX | 52 | 42 | 
Windows (U-Value/SHGC) | U-0.18, 0.29 SHGC | U-0.28, 0.29 SHGC | -$5,343
DHW | Gas Tankless 0.94 EF | HPWH, 50 gal | -$316
Heating | Gas, 95% AFUE | SEER 20, 12 HSPF, Ductless | -$2,487
Cooling | SEER 14.2 |  | 
Duct Leakage to Outside | 2 CFM25 per 100ft2, R-6 | Ductless | -$6,749
Foundation Insulation | NA | NA | $0
Floor Insulation | Basement Ceiling R-30 | Basement Ceiling R-30 | $0
Wall Insulation | R-21, 2x6, 16 in o.c. | R-21, 2x6, 16 in o.c. | $0
High Efficacy Lighting | 100% LED | 100% LED | $0
Ceiling Insulation | Ceiling R-49, Vented | Roof R-38 Spray Foam, Unvented | $2,511
Air Infiltration | 3 ACH50 | 2 ACH50 | $787
Mechanical Ventilation | HRV, 75% | HRV, 75% | $0
Pre-Wiring5 | N/A | N/A | $0
Solar Array5 | N/A | N/A | $0
TOTAL |  |  | -$11,597
Additional Costs are the costs above Base Code to reach Stretch Code.
Cost included in basement and/or attic thermal boundary change
Base Code home features are based on an analysis of typical practices for achieving a HERS 52 using HERS Provider data on pre viously built
homes in Massachusetts.
Stretch Code home features are based on cost optimization modeling using BEopt software. Some individual features are less efficient than the Base Code home, but they are more than offset by other features that are more efficient. One benefit of using a HERS Index target as the basis of the Stretch Code is that it give builders the flexibility to make different design choice to allow for optimization of cost effec tiveness, work around other design constraints, and accommodate client-specific requests. The stretch code model was developed used REM/rate Version 16.1.1.
Pre-wiring and solar costs are only applicable to mixed fuel projects following the Specialized code and do not apply to the Base or Stretch Code.
Breakdown of Construction Costs to Meet Stretch Code
2100 ft2 Small Single Family
3 Bedroom - Worcester, MA
Electric
Heat Pump
HERS Index (ERI)
52 42
Base Stretch

## Slide 43: Small Single Family - Gas
MA 10th Edition Building Code | 2025
 | COSTS |  | BENEFITS6 | NET
Total Added Construction Costs | $14,064 Extra Costs |  | $2,500 Rebates1,4 | $11,564 Cost Compared to Base Code
HOME BUYER | $1,156 Increase in Downpayment3 | $777 Increase in Annual Mortgage Payment3 | $190 Estimated Additional Energy Costs per Year2 | $967 Buyer Annual Net
1. Rebates are calculated on a per unit basis, using Mass Save ® new construction program Base Tier Incentives of $7,500 without any Market Transformation Adders. These incentives are not applicable to mixed fuel projects.
Energy costs are based on 28.7 cents/kWh, $2.08/therm, and $3.62/gal propane
30-year mortgage assumes 10% down payment at 6.35% APR
In addition to the Mass Save ® rebates, projects may be eligible for $2,500/unit rebate as part of the 45L Federal Tax Credit.
Mass Save Incentives are not available in communities with municipal light plants, which are locally owned utilities which represent 52 towns that make up about 13% of the MA population
Costs and Benefits to Meet Stretch Code*
Home Details
2100 ft2
Small Single Family
3 Bedrooms
Worcester, MA
Gas
HERS Index (ERI)
52 42
Base Stretch
*Green shaded boxes indicate cost savings, while red shaded boxes indicate added costs.

## Slide 44: Small Single Family - Gas
MA 10th Edition Building Code | 2025
FEATURE | BASE CODE3 | STRETCH CODE4 | COST DIFFERENTIAL1
HERS INDEX | 52 | 42 | 
Windows (U-Value/SHGC) | U-0.18, 0.29 SHGC | U-0.18, 0.29 SHGC | $0
DHW | Gas Tankless 0.94 EF | Gas Tankless 0.94 EF | $0
Heating | Gas, 95% AFUE | Gas, 98% AFUE | $708
Cooling | SEER 14.2 | SEER 16 | $671
Duct Leakage to Outside | 2 CFM25 per 100ft2, R-6 | In Finished Space* | $0
Foundation Insulation | NA | Basement Walls R-21 | $6,547
Floor Insulation | Basement Ceiling R-30 | NA | -$1,426
Walls Insulation | R-21, 2x6, 16 in o.c. | R-21, 2x6, 16 in o.c. R-5 XPS | $3,015
High Efficacy Lighting | 100% LED | 100% LED | $0
Ceiling Insulation | Ceiling R-49, Vented | Roof R-38 Spray Foam, Unvented | $2,187
Air Infiltration | 3 ACH50 | 1 ACH50 | $2,362
Mechanical Ventilation | HRV, 75% | HRV, 75% | $0
Pre-Wiring5 | N/A | N/A | $0
Solar Array5 | N/A | N/A | $0
TOTAL |  |  | $14,064
Additional Cost are the costs above Base Code to reach Stretch Cod e.
Cost included in basement and/or attic thermal boundary change
Base Code home features are based on an analysis of typical practices for achieving a HERS 52 using HERS Provider data on pre viously built homes
in Massachusetts.
Stretch Code home features are based on cost optimization modeling using BEopt software. Some individual features are less efficient than the Base Code home, but they are more than offset by other features that are more efficient. One benefit of using a HERS Index target as the basis of the Stretch Code is that it give builders the flexibility to make different design choice to allow for optimization of cost effec tiveness, work around other design constraints, and accommodate client-specific requests. The stretch code model was developed used REM/rate Version 16.1.1.
Pre-wiring and solar costs are only applicable to mixed fuel projects following the Specialized code and do not apply to the Base or Stretch Code.
Breakdown of Construction Costs to Meet Stretch Code
Gas
2100 ft2 Small Single Family
3 Bedroom - Worcester, MA
HERS Index (ERI)
52 42
Base Stretch

## Slide 45
Appendix C
Commercial Cost Analysis -Comparing the Base Code to Stretch Energy Code

## Slide 46
Table of Contents
Summary of 2023 Stretch Code
Cost impacts by building type
Recent updates to the Stretch Energy Code

## Slide 47
Summary
The 2023 Stretch Code is a thermal code
  Focuses on minimizing heating demand
  Results on large energy (and cost) savings
Energy savings mean lower life cycle costs
  In some cases, first costs are LOWER than under the old stretch code
  Incentives and low-cost financing drive down costs even further
Updates in February 2025 create more flexibility
  Relaxed requirements for existing buildings
  New low-carbon construction credit

## Slide 48
Mid-rise multifamily (slab-on-grade)
Stretch Code cost compared to Base Code (% difference) | First Cost | 50-year lifecycle
Natural gas | 1.7% | -2.2%
All-electric | 0.7% | -5.6%
Notes: Multi-family building with 63,200 sf in four-stories and 58 apartments
• Current Energy Code Design reflects industry standards including:
o Metal panel rainscreen system with wood frame back-up wall
o In-unit gas fired combination (heating + domestic hot water) units
• Optimized Design (NG) scenario includes in-unit gas fired combination (heating + domestic hot water) units & an improved envelope
• Optimized Design (Elec) scenario includes air source heat pump systems, electric resistance SHW & an improved envelope

## Slide 49
Mid-rise multifamily (podium)
Stretch Code cost compared to Base Code (% difference) | First Cost | 50-year lifecycle
Natural gas | 2.6% | -0.6%
All-electric | 3.2% | -1.9%
Notes: Multi-family building with 71,100 sf in eight-stories and 81 apartments
• Current Energy Code design reflects industry standards including:
o Metal panel rainscreen system with steel frame back-up wall
o Gas fired packaged vertical units
o Gas fired domestic hot water (DHW)
• Optimized Design (NG) scenario includes gas fired packaged vertical units; gas fired DHW & an improved envelope
• Optimized Design (Elec) scenario includes air source heat pump systems, heat pump water heater (DHW) & an improved envelope

## Slide 50
High-rise multifamily
Stretch Code cost compared to Base Code (% difference) | First Cost | 50-year lifecycle
Natural gas | 3.9% | -2.0%
All-electric | 4.2% | -1.7%
Notes: 267,100 sf in twenty-six stories and 352 apartments
• Current Energy Code Design reflects industry standards including:
o Metal panel rainscreen system with steel frame back-up wall
o Water source heat pumps, gas boiler & domestic hot water (DHW)
• Optimized Design (NG) scenario includes WSHPs, gas boiler and DHW, & an improved envelope
• Optimized Design (Elec) scenario includes WSHPs, heat pump boilers, heat pump DHW heaters & an improved envelope

## Slide 51
Small office
Stretch Code cost compared to Base Code (% difference) | First Cost | 50-year lifecycle
Natural gas | 3.3% | -0.7%
All-electric | 4.5% | -0.2%
Notes: Office building with 25,200 sf in two-stories
• Current Energy Code Design reflects industry standards including:
o Rainscreen system with brick and metal stud back-up, 40% WWR
o Packaged rooftop gas-fired HVAC system
o Electric SHW
• Optimized Design (NG) scenario includes DOAS with ERV, gas-fired heating system, & electric SHW
• Optimized Design (Elec) scenario includes DOAS with ERV, electric heat pump system, & electric SHW

## Slide 52
Large office
Stretch Code cost compared to Base Code (% difference) | First Cost | 50-year lifecycle
Natural gas | -4.6% | -8.7%
All-electric | -4.0% | -8.3%
Notes: Savings likely from moving from hydronic baseboard to DOAS w/ ERV
Office building with 614,400 sf in 15 stories
• Current Energy Code Design reflects industry standards including:
o Curtain wall system (modular) with metal finish spandrel panels
o Central air handling units, hydronic baseboards, VAVs
o Electric SHW
• Optimized Design (NG) scenario includes DOAS with ERV, gas-fired heating system, fan coil units & electric SHW
• Optimized Design (Elec) scenario includes DOAS with ERV, electric heat pump boiler system, fan coil units & electric SHW

## Slide 53
Office and lab
Stretch Code cost compared to Base Code (% difference) | First Cost | 50-year lifecycle
Natural gas | -1.1% | -6.0%
All-electric | -0.6% | -6.3%
Notes: Savings likely from moving from hydronic baseboard to DOAS w/ ERV
Office-lab (55/45) building with 422,400 sf in 9 stories (+2 below grade)
• Current Energy Code Design reflects industry standards including:
o Curtain wall system (modular) with metal finish spandrel panels
o Central air handling units, hydronic baseboards, VAVs, electric SHW
• Optimized Design (NG) scenario: DOAS with ERV, gas-fired heating system, fan coil units electric SHW, improved curtainwall performance
• Optimized Design (Elec) scenario: DOAS with ERV, electric heat pump boiler system, fan coil units, electric SHW, improved curtainwall performance

## Slide 54
Elementary school
Stretch Code cost compared to Base Code (% difference) | First Cost | 50-year lifecycle
Natural gas | 0.2% | -1.4%
Electric + NG hot water | 0.8% | -1.9%
Notes: Primary school with 73,960 sf in 2 stories
• Current Energy Code Design reflects industry standards including:
o Brick wall with steel frame backup wall
o Central air handling units + hydronic BB, VAVs, packaged RTUs
o Natural gas SHW
• Optimized Design (NG) scenario includes ERV on Central Air Handler, gas-fired heating system, fan coil units & natural gas SHW
• Optimized Design (Elec) scenario includes DOAS with ERV, variable refrigerant flow (VRF) heating and cooling system & natural gas SHW

## Slide 55
Middle/High school
Stretch Code cost compared to Base Code (% difference) | First Cost | 50-year lifecycle
Natural gas | 0.2% | -2.3%
Electric + NG hot water | 0.8% | -2.5%
Notes: Secondary school with 328,000 sf in 4 stories
• Current Energy Code Design reflects industry standards including:
o Brick veneer with steel frame backup wall
o Central air handling units & hydronic BB, VAVs, packaged RTUs
o Natural gas SHW
• Optimized Design (NG) scenario includes DOAS with ERV, gas-fired heating system, fan coil units & natural gas SHW
• Optimized Design (Elec) scenario includes DOAS with ERV, electric heat pump boiler system, fan coil units & natural gas SHW

## Slide 56
Lisa Sullivan
Green Communities
Southeast Regional Coordinator
Cell: (617)312-4018
Email: Lisa.m.sullivan@mass.gov
www.mass.gov/orgs/green-communities-division